OLED Panel
- I²C slave operating at 100kHz or 400kHz
- Reports input events in an event FIFO
- Rotary encoder quadrature decode
- Button press debounce
- LED PWM brightness control
- Piezo sounder tone generation
- 4 GPIO lines capable of output or input, including change reporting
# Basic Operation
The control chip on an OLED Panel Module is a self-contained microcontroller accessible as an I²C slave. This chip handles operation of the rotary encoder and push-buttons, LEDs, piezo sounder, and GPIO header on the board.
The chip responds to wheel rotation and press events, and can autonomously drive the piezo sounder to make a beep sound when these occur, independently of the host MCU.
An 8-level FIFO of events is maintained, which reports input events on the rotary encoder or changes in state of the GPIO lines. Whenever this FIFO is non-empty, the INT output line is pulled low. When the FIFO is emptied, the INT line is returned to hi-Z state.
# I²C Operation
The control chip is accessed via a standard I²C bus, which can operate at 100kHz or 400kHz. The 1MHz "fast mode" is not supported. The default slave address is 0x3D (0x7A write, 0x7B read).
The chip makes use of SCL clock stretching to insert delays on the bus when it requires extra time to respond, so needs a bus master that can accept this. If any bus isolation or multiplexing is used, that too will need to support SCL clock stretching by slaves.
The chip operates as a simple register-based slave, containing a set of individually-numbered registers. Each register may be read or written to (though some registers are notionally read-only, and attempts to write will be ignored).
## Register Writes
Registers may be written to in a single WRITE transaction, consisting of a START condition, slave-addressing byte, register address, value, and STOP condition.
START	Slave (W)	ACK	Addr	ACK	Value	ACK	STOP
	Master sends the slave writing address; 0x7A		Master sends a register number - see the section below		Master sends the new value for the register

## Register Reads
Registers may be read from in a single WRITE-then-READ transaction, consisting of a START, slave-addressing byte, register address, repeated START, another slave-addressing byte, reading the value, STOP.

START	Slave (W)	ACK	Addr	ACK	RE-START	Slave (R)	ACK	Value	ACK	STOP
	Master sends the slave writing address; 0x7A		Master sends a register number - see the section below			Master sends the slave reading address; 0x7B		Slave sends the current value of the register

## Detailed Register List
## EVENT
Address: 0x01
Direction: R
Default value: 0x00
Implements an 8-level deep FIFO of input events. Each event is formed of a single byte. The top three bits of the event classify it into a category, the remaining bits are specific to that category.
0b000xxxxx	No event 0b00000000 / 0x00
0b001xxxxx	Wheel rotation: lower bits give the wheel direction 0b001xxx01 / 0x21 - wheel downwards (anticlockwise) 0b001xxx10 / 0x22 - wheel upwards (clockwise) next three bits identify increments (when ‘encoder acceleration’ option is enabled) / 0b001000xx / 0x20 to 0b001111xx / 0x3C – 1 to 8 increments
0b010xxxxx	Button: lowest bit gives the button press/release state 0b010xxx00 / 0x40 - button release 0b010xxx01 / 0x41 - button press 0b010xxx10 / 0x42 - button held next three bits identify the button 0b010000xx / 0x40 - wheel button 0b010001xx / 0x44 - main button 0b010010xx / 0x48 - left soft button 0b010011xx / 0x4C - right soft button
0b011xxxxx	GPIO state change: lower 4 bits give the GPIO line state at the time the event occurred 0b01100000 / 0x60 to 0b00101111 / 0x6F - GPIO state captured

When an input event occurs, the INT line will be pulled low. Reading from this register will clear the event from the queue, causing the next to appear. If there are no more events waiting, the register will read as zero and the INT line will be returned to high impedance state.
## RELEASEMASK
Address: 0x02
Direction: R/W
Default value: 0x00
Controls whether buttons will send event reports on release as well as press (bits set to 1), or on press only (bits set to 0).
0b.......x	Ignored
0b......x.	Wheel button
0b.....x..	Main button
0b....x...	Left soft button
0b...x....	Right soft button

## DEBOUNCE_TIME
Address: 0x03
Direction: R/W
Default value: 0x14 / 20
Gives the duration in milliseconds for key debounce detection.
## BTNHOLD_TIME
Address: 0x04
Direction: R/W
Default value: 0x4b / 75
Gives the duration in centiseconds for reporting a "button held" event.
## KEYBEEP_DURATION
Address: 0x10
Direction: R/W
Default value: 0x0A / 10
Gives the duration in centiseconds for an autonomous keybeep.
## KEYBEEP_MASK
Address: 0x11
Direction: R/W
Default value: 0x00
Controls which button events cause an autonomous keybeep.
0b.......x	Wheel rotation
0b......x.	Wheel button
0b.....x..	Main button
0b....x...	Left soft button
0b...x....	Right soft button

## BEEP_DURATION
Address: 0x12
Direction: R/W
Default value: 0x00
Writing a non-zero value into this register will immediately cause a beep of the given duration, in centiseconds. Reading the value will give a current countdown of the remaining time for the ongoing beep.
## BEEP_TONE
Address: 0x13
Direction: R/W
Default value: 0xC8 / 200
Sets the frequency of the beep tone, in units of 10Hz. The default value of 200 sets a tone of 2kHz, which is ideal for the piezo sounder being used. Note that altering this value will also change the tone used by the autonomous keybeep.
## BEEP_FREQ
Address: 0x14-0x15
Direction: R/W
Default value: 0x07D0 / 2000
A 16bit big-endian alternative to the BEEP_TONE register, which sets the frequency of the beep tone, in units of 1Hz. The default value of 2000 sets a tone of 2kHz, which is ideal for the piezo sounder being used. Note that altering this value will also change the tone used by the autonomous keybeep.
## LED1_PWM
Address: 0x20
Direction: R/W
Default value: 0x00
Sets the brightness of LED1, which is connected to the red LED in the main button. The default value of 0 is off, and 255 is full brightness. Values in-between will be pulse-width modulated at a frequency of around 4kHz.
## LED2_PWM
Address: 0x21
Direction: R/W
Default value: 0x00
Sets the brightness of LED2, which is connected to the green LED in the main button. The default value of 0 is off, and 255 is full brightness. Values in-between will be pulse-width modulated at a frequency of around 4kHz.
## GPIO_DIR
Address: 0x30
Direction: R/W
Default value: 0x00
Sets the drive direction on each of the GPIO lines. Bits set low (0) are inputs; set high (1) are outputs. The lower four bits are used; the upper four are ignored.
## GPIO_IO
Address: 0x31
Direction: R/W
Default value: 0x00
Writes to this register set the output state for any GPIO lines currently set as outputs. The state of pins set as inputs is ignored. The lower four bits are used; the upper four are ignored.
Reads from this register return the current state of all four GPIO lines, regardless of drive state.
## GPIO_PULLUP
Address: 0x32
Direction: R/W
Default value: 0x00
Enables pullup resistors on any of the GPIO lines with bits set high (1). This pullup is about 50kohm; sufficient to hold a high state around a button or similar input. The lower four bits are used; the upper four are ignored.
## GPIO_EVENTMASK
Address: 0x33
Direction: R/W
Default value: 0x00
Sets a mask used for level change event detection on the GPIO lines. A change of state on any lines which are set as inputs and have the mask bit high (1) will be reported as a GPIO event into the event FIFO. This event will capture the current value of all four lines at the time the level changed.
## SWVERSION
Address: 0xF0
Direction: R
Default value: 0x02 / 2
Reports the driver software version.
# EEPROM STORED PARAMETERS (active after next reset)
## I2CADDRESS
Address: 0xC0
Direction: R/W
Default value: 0x3D / 61
Set the i2c address used to communicate with the panel
## OPTIONS
Address: 0xC1
Direction: R/W
Default value: 0x00 / 0
0b.......x	Enable encoder acceleration
0bx.......	Reverse encoder direction

## DEBOUNCE_TIME
Address: 0xC2
Direction: R/W
Default value: 0x14 / 20
Gives the duration in milliseconds for key debounce detection.
## BTNHOLD_TIME
Address: 0xC3
Direction: R/W
Default value: 0x4b / 75
Gives the duration in centiseconds for reporting a "button held" event.
## REMAP_MASK
Address: 0xC4
Direction: R/W
Default value: 0x00 / 0
Redirect buttons status to GPIO pins
0b.......x	Wheel button on GPIO0
0b......x.	Main button on GPIO1
0b.....x..	Left soft button on GPIO2
0b....x...	Right soft button on GPIO3

## REMAP_POLARITY
Address: 0xC5
Direction: R/W
Default value: 0x00 / 0
Change polarity for redirected keys
## ENCODER_ACC
Address: 0xC6
Direction: R/W
Default value: 0x19 / 25
Increment factor for wheel steps
## ENCODER_DEC
Address: 0xC7
Direction: R/W
Default value: 0x02 / 2
Decrement factor for wheel steps